## Slide 1: DC Biasing – BJTs
Topic 4 (Chapter 4) (Some materials are from Malvino’s book)

## Slide 2
Biasing
Biasing: Applying DC voltages to a transistor in order to turn it on so that it can amplify AC signals.

## Slide 3
4.2 Operating Point
The DC voltages establishes an operating or quiescent point
called the Q-point.

## Slide 4
The Three Operating Regions
    Active or Linear Region Operation
    Base–Emitter junction is forward biased
        Base–Collector junction is reverse biased
        BJT works as an Amplifier
    Cutoff Region Operation
    Base–Emitter junction is reverse biased
    Base–Collector junction is reverse biased
    BJT works as an OFF Switch
    Saturation Region Operation
    Base–Emitter junction is forward biased
    Base–Collector junction is forward biased or near forward bias
    BJT works as an ON Switch

## Slide 5: Regions of operation
Active - - - used for linear amplification
Cutoff - - - used in switching applications (OFF)
Saturation - - - used in switching applications (ON)
Breakdown - - - can destroy the transistor and should be avoided
Cutoff Region

## Slide 6
DC Biasing Circuits
Fixed-bias or Base-Bias
Emitter Bias
Voltage divider bias circuit
DC bias with voltage feedback

## Slide 7: 4.3 Base-Bias or Fixed-Bias
Setting up a fixed value of base current
Base current remains constant for given values of VBB
Usually VBB and VCC
are the same supply
VCC
RC
RB
VBB
12 V
1 kW
12 V
VCE

## Slide 8: Load line
A visual summary of all the possible transistor operating points
Connects saturation current (ICsat) to cutoff voltage (VCEcutoff )

## Slide 9
0
2
4
6
8
10
12
14
16
18
2
4
6
8
10
12
14
VCE in Volts
IC in mA
20 mA
0 mA
100 mA
80 mA
60 mA
40 mA
IC =
VCC - VCE
RC
A graph of this equation
produces a load line.
Load line

## Slide 10
Saturation
When the transistor is operating in saturation, current through the transistor is at its maximum possible value.

## Slide 11
VCC
RC
RB
VBB
12 V
1 kW
12 V
Mental
short
IC =
12 V
1 kW
Understanding Saturation

## Slide 12
0
2
4
6
8
10
12
14
16
18
2
4
6
8
10
12
14
VCE in Volts
IC in mA
20 mA
0 mA
100 mA
80 mA
60 mA
40 mA
IC =
12 V
1 kW
= 12 mA
This is the
Saturation (maximum) current.
Understanding Saturation

## Slide 13
VCC
RC
RB
VBB
12 V
1 kW
12 V
Mental
open
Understanding Cutoff

## Slide 14
0
2
4
6
8
10
12
14
16
18
2
4
6
8
10
12
14
VCE in Volts
IC in mA
20 mA
0 mA
100 mA
80 mA
60 mA
40 mA
VCE(cutoff) = VCC
Understanding Cutoff

## Slide 16
VCC
RC
RE
VBB
5 V
1 kW
15 V
1 kW
2.2 kW
IE =
VBB - VBE
RE
= 1.95 mA
VC = 15 V - (1.95 mA)(1 kW) = 13.1 V
4.4 Emitter bias:
Contains an emitter resistor
VCE = 13.1 V - 4.3 V = 8.8 V
IC @ IE

## Slide 17: BJT DC biasing
First give appropriate directions of the three currents (, and )
Find
Apply KVL in the base-emitter loop. . Find
Find and from
Apply KVL in the collector-emitter loop. Find
Apply KVL in the base loop to find
. Find
. Find
Apply KVL in the emitter loop to find

## Slide 20
+VCC
RC
RE
R1
R2
4.5 Voltage divider bias
Base circuit contains a voltage divider
Most widely used
Known as VDB

## Slide 21
+VCC
RC
RE
R1
R2
Voltage divider bias circuit
{
R1 and R2 form
a voltage divider

## Slide 22
Divider analysis:
Rth = R1 || R2
R2
R1 + R2
VCC
Eth =

## Slide 24
4.6 Collector-feedback bias
Our text calls it DC Bias With Voltage Feedback
Current through